Random things.....

---
2D Fit
- Following Chris’ suggestion, write tail part as
  - (b x y – 1) exp(-b x y)
  - b = parameter b
  - x = MR – MR0
  - y = R^2 – R20
- Fit to the tail part only

---
1-component fit

---
Some bias detected!
- b = 0.017 +- 0.032, sigma 0.966 +- 0.022
- MROffset = 0.060 +- 0.032, sigma 0.969 +- 0.025
- R2Offset = 0.084 +- 0.033, sigma 0.997 +- 0.024

---
Still working on two-component fit
- Seems to be working, but some bias (a bit larger than one-component case) seen.
- Will double-check for now

---
Some pretty plots